## Slide 1
A Study of the Polarization Dependency of Raman Spectra
Jonas Eichhorn
Jonas Eichhorn

## Slide 2
Biological Applications of Raman Spectroscopy
Jonas Eichhorn
Complex Spectra
Machine Learning
Sensitive Model
…
A.A. Moawad, A. Silge, et. al., Molecules, 24, 24, 4516 (2019).
Notes: Task:
Distinguish very similar spectra of related bacteria
Solution:
Machine Learning can identify small differences in spectra
Problem:
Model must be very sensitive to distinguish bacteria
Different Raman spectrometers generate slighlty different spectra
Model can‘t distinguish influence of spectrometer and changes caused by different samples
Question of the thesis:
Wide-spread clinical application is difficult (model transfer methods, repairs/replacements, data sharing)
Is the polarisation of the exciting laser one reason why we can‘t compare Raman spectra from different Raman spectrometers?

## Slide 3
Polarisation Dependency in Raman
Jonas Eichhorn
Notes: EM-Wave:
Electric and a Magnetic component
For simplification: Only the electric component will be discussed
Polarisation:
Looking at the electrical component: Oscillation can happen in all directions -> unpolarised light
Oscillating electrical fields can be correlated -> polarised light
Circular polarisation possible, but not relevant for this
Notation:
Electromagnetic wave as oscillating e-field vector
Polarisation as 4-D Stokes vector
Raman Scattering:
Molecules have anisotropic polarisabilities -> anisotropic changes of polarisability
Polarisation of the exciting wave influences: polarisation of scattered light and scattering efficience

## Slide 4
Polarisation Dependent Behaviour
Jonas Eichhorn
laser
detector and
spectrograph
microscope
with sample
fiberbench
Characterise Fiber
Manipulate Polarisation
Characterise
Fiber
fiberbench
laser
sample
wave plate
Characterise
Spectrograph
Notes: Why should we worry about polarisation dependency of Raman scattering?
Fiber-coupled Raman microscope was used
Spectrometer has polarisation sensitive optical grating
Reflectance and polarisation of reflected light depends on intial state of polarisation
Furthermore optical fibers have influence on polarisation
Idea: Simulate different Raman spectrometer with one device
Characterise polarisation dependency of fibers and spectrograph
Manipulate state of polarisation with optical element -> rotate plane of polarisation
Fiberbench placed between laser and microscope

## Slide 5
Characterisation of Optical Fibers: Degree of Polarisation
Jonas Eichhorn
Degree of polarisation depends on the polarisation!
Notes: All optical fibers reduce the degree of polarisation
Complex polarisation dependent behaviour
MM-Fiber F3 seems to have periodic dependency
Depolarisation should decrease the magnitude of polarisation dependent effects
This makes it difficult to measure the effect

## Slide 6
Characterisation of Optical Fibers: Mueller matrix
Jonas Eichhorn
Laser
Fiber
Fiber
Notes: Describe optical fibers mathematically:
Why the math? -> simulate and validate experiments later on
Applying 4x4 Mueller matrix onto Stokes vector describes light-matter interaction
Mueller matrix describes influence of fiber on state of polarisation
How to compute Mueller matrix?
Measure Stokes vectors before and after fiber
Build non-linear model to fit the data with the matrix elements
Result:
Matrix of SM-fiber describes the changing stokes vectors good
Degree of polarisation is poorly described
Matrix can‘t be used, instead only characterised states of polarisation will be used in later experiments
MM-fiber is described very good by Mueller matrix. Stokes parameter and degree of polarisation are fitted well

## Slide 7
Characterisation of the Spectrometer: White Lamp Spectra
Jonas Eichhorn
Complex Polarisation Dependent Behaviour
Notes: White Lamp Spectra
Spectrometer was characterised with linear polarised white lamp
Characterisation with and without microscope & optical fiber
The sensitivity of the detector depends on the polarisation
Optical fiber and microscope decrease intensity and introduce artifacts
Difference Spectra
The polarisation dependency increases with the wavenumber
Change in polarisation sensitivity is stepwise, non linear and polarisation dependent

## Slide 8
Characterisation of the Spectrometer: CCl4
Jonas Eichhorn
Notes: Characterise spectrometer with Tetra
Why Tetra? -> Good scatterer and high polarisation dependence
Result
Signal strength changes periodically with the rotation of the plane of polarisation
peak height ratio changes -> potential problem for analysis

## Slide 9
Raman-Mueller-Transformation: A Reminder
Jonas Eichhorn
QC Calculation
Raman Tensor
Mueller Matrix
F2 
Notes: Derived in previous talk
Fully and linear polarised light was assumed
Characterisation shows: The experiment does not satisfy the assumptions.

## Slide 10
Generalising the Derivation
Jonas Eichhorn
Linear Combination
Integration
Apply Raman-Mueller-Matrix
Notes: (Point at formula when you talk!)
Express the linear Stokes vector as linear combination of a totally polarised and a totally unpolarised part.

## Slide 11
Generalising the Derivation
Jonas Eichhorn
Linear Combination
Integration
Apply Raman-Mueller-Matrix
Notes: Express the Stokes vector of the unpolarised part with polarised Stokes vectors.
Use all totally linear polarised Stokes vectors
Combination of all vectors yields unpolarised light
Expressed as Integral over polar Stokes parameter

## Slide 12
Generalising the Derivation
Jonas Eichhorn
Linear Combination
Integration
Apply Raman-Mueller-Matrix
Notes: Applying Mueller matrix onto linear combination and partially polarised Stokes vector are equivalent
Raman-Mueller-Transformation can be applyed for partially polarised light

## Slide 13
Simulation of Raman Spectra: CCl4
Jonas Eichhorn
Non-Linear Model
Notes: Simulate Detector response D for validating Raman spectra of tetra
Assumption: detector has one sensitive optical axis
I_y is the lights intensity along the sensitive optical axis
I_x is the lights intensity perpendicular to the sensitive optical axis
Input and Output
Intensities are computed from Stokes vectors
D is derived from measured Raman spectra
Stokes parameter is computed from characterised Stokes vector, Raman-Mueller-matrix and Mueller matrix of the MM-fiber
A describes the anisotropy of the detector
A is computed with non-linear model
A=1 is isotropic detector, A>1 y-axis is the sensitive optical axis

## Slide 14
Simulation of Raman Spectra: CCl4
Jonas Eichhorn
/ cm-1 |  |  | 
222,911 | 1,488 | 1,120 | 1,079
318,980 | 1,534 | 1,067 | 1,090
463,676 | 0,949 | 1,074 | 1,110
794,060 | 1,003 | 1,068 | 1,154
222,911 | 1,488 | 1,120 | 1,079
318,980 | 1,534 | 1,067 | 1,090
463,676 | 0,949 | 1,074 | 1,110
794,060 | 1,003 | 1,068 | 1,154
<
<
<
<
>
>
>
Why is the anisotropy to big/small?
Rayleigh Filter
Microscope
Vector Normalisation
Noise
Notes: Compare A derived from Tetra with A derived from white lamp spectra:
Expected: A_Det > D_Dert,coupled > A_CCl4
optical fibers depolarise -> less polarisation dependency expected
Result:
222/cm: A is bad, because Rayleight filter; Fit is good
318/cm: A is bad; Fit is good
463/cm: A is very bad; Fit is good
A<1 would mean that I_x is for only one peak more sensitive -> physics says NO
765/cm ignored because Gaussian can‘t handle combinatory vibrations
794/cm: A is good; Fit is bad, propablly because Noise?
Possible Reasons for unexpected results:
Rayleigh filter edge
Uncharacterised microscope
All spectra were normalised individually
Normalisation on polarisation independent peak would have been better, but physics says NO
Noise

## Slide 15
Polarisation Dependent Raman Spectra
Jonas Eichhorn
Notes: Shortly investigate influence on biologically relevant samples:
4-AAP, Phe, Trialaurin
Polarisation dependency negelibe
Phe and Trilaurin show fiber artifacts and complex background
Analysis of spectra difficult

## Slide 16
Conclusion
Jonas Eichhorn
Quantification
Mueller formalism enbles quanti-fication of the polarisation depen-dency of a system
Optical Fibers
Optical fibers have a great influence on the state of polarisation
Spectrometers
Polarisation depen-dency is negligible
Outlook
Control of polarisation states needs to be improved
Long MM-fiber might remove pol-arisation depen-dency
Arbitrary polarisa-tion states could not be generated
Fiber-coupled Sys-tems are probably not affected
Depolarisation of the laser doesn‘t support definitive conclusions
Test free-space systems
Polarisation dependent standard samples if necessary

## Slide 17
Jonas Eichhorn
Thank you
for your attention!